## Slide 1
Parameter | Description | Specification | Unit
 | Input voltage |  | 
 | Output voltage |  | 
 | Reference voltage from Bandgap |  | 
 | Min supply voltage |  | 
 | Resistor loading |  | 
Temp | Simulation temperature |  | 
Corner, Tech |  | Typical, tsmc 65nm | 
Device type |  | pch/nch_lvt | 
Parameter | Description | Specification | Unit
 | Input voltage |  | 
 | Output voltage |  | 
 | Reference voltage from Bandgap |  | 
 | Min supply voltage |  | 
 | Resistor loading |  | 
Temp | Simulation temperature |  | 
Corner, Tech |  | Typical, tsmc 65nm | 
Device type |  | pch/nch_lvt | 
SIMULATION CONDITION

## Slide 2
Testbench | Parameter | Description | Specification | Unit
DC |  | Overdrive voltage (Vgs – Vth) | for all mosfet | 
 |  | Margin voltage (Vds-Vdsat) | for all mosfet | 
Transient |  | Output voltage error |  | 
 |  | Line regulation, variation of Vin |  | 
 |  | Load regulation, iload varies from max to min |  | 
AC |  | Unity Gain Bw |  | 
 |  | DC Loop Gain |  | 
 |  | Phase Margin of loop |  | 
 |  | Power Supply Rejected Ratio |  | 
Testbench | Parameter | Description | Specification | Unit
DC |  | Overdrive voltage (Vgs – Vth) |  | 
 |  | Margin voltage (Vds-Vdsat) |  | 
Transient |  | Output voltage error |  | 
 |  | Load regulation, iload varies from max to min |  | 
AC |  | Unity Gain Bw |  | 
 |  | DC Loop Gain |  | 
 |  | Phase Margin of loop |  | 
 |  | Power Supply Rejected Ratio |  | 
LDO SPECIFICATION

## Slide 3
BIAS
1.1 Should choose R1~kOhm to reduce static current as much as possible (recommend: 30kOhm) 1.2 R0 should be chosen around ~kOhm (1-500kOhm)
2. These 2 devices must have the same dimension (fg & stk).
3. These 2 devices must be the same (fg & stk), no need to be as same as (2)
4. They need to have specific ratios b/w each pair
And k, m must be integer numbers

## Slide 4
BIAS
1.1 Should choose R1~kOhm to reduce static current as much as possible (recommend: 30kOhm) 1.2 R0 should be chosen around ~kOhm (1-500kOhm)
Constraint of variable names |  |  |  | 
Device | L (m) | Number of finger | Multiplier | Range of value
R0 |  |  |  | 
MN1 | stk_bias_n1*60n | fg_bias_n1 | 1 | 
MN2 | stk_bias_n2*60n | fg_bias_n2 | 1 | 
MN3 |  |  | 1 | 
MP1 | stk_bias_p1*60n | fg_bias_p1 | 1 | 
MP2 |  |  | 1 | 
MP3 | stk_bias_p3*60n | fg_bias_p3 | 1 | 
MP4 |  |  | 1 | 
Constraint of variable names |  |  |  | 
Device | L (m) | Number of finger | Multiplier | Range of value
R0 |  |  |  | 
MN1 | stk_bias_n1*60n | fg_bias_n1 | 1 | 
MN2 | stk_bias_n2*60n | fg_bias_n2 | 1 | 
MN3 |  |  | 1 | 
MP1 | stk_bias_p1*60n | fg_bias_p1 | 1 | 
MP2 |  |  | 1 | 
MP3 | stk_bias_p3*60n | fg_bias_p3 | 1 | 
MP4 |  |  | 1 | 
**Note: - Resistance of R0 is
-  fixed value
UPDATE
** finger width = 200n

## Slide 5
BIAS - example
Total length = stk * 60n (stk is integer number (1, 2, …)
Min finger width
n.o fingers, *0.5 means we want 60n per step
Keep multi=1
Automatically adjust
Reference transistor size
Variable name
stk_core_p1 fp_core_p1
stk_core_p3 fp_core_p3
stk_core_n2 fp_core_n2
stk_core_n1 fp_core_n1
** must follow variable name when applying optimization algorithms

## Slide 6
BIAS - example
DCOP check:
Static current through 1st branch ~ .
Base current of BIAS circuit is .
All mosfets operate in saturation/sub-threshold region
DCOP condition:
  Region = 2 (saturation) or 3 (sub-threshold)
  Overdrive voltage
  Voltage margin
How to check?  DCOP verification sequence
If region = 2  PASS DCOP
If region = 3  check
  If
  Else  FAIL DCOP check
i_check
We have: we need this value around as base current
Allowable value range:
Testbench | Parameter | Description | Specification | Unit
DC |  | Operation region | (follow the verification sequence above) | 
 |  | Base current |  | 
Testbench | Parameter | Description | Specification | Unit
DC |  | Operation region |  | 
 |  | Base current |  | 

## Slide 7
BIAS - example
Example of DCOP check of 1 device  need to check all devices in schematic
Testbench setup
Cell name
Name of parameters
Measurement  can include in OCEAN file to do the simualtion
measurement
 DCOP analysis
After pass all the requirement (DCOP, i_check)

## Slide 8
Core
2. Replace 2 identical core PMOS by 2 ideal current source having same current value
1. Must be the same (fg & stk)
Ibp=i0
i1
i2
i2
Ibn=i3
i1
Ibp=i0
3. These 2 devices must be the same (fg & stk), no need to be as same as other pair
5. These 2 devices must be the same (fg & stk), no need to be as same as other pair
6. These 2 devices must be the same (fg & stk), no need to be as same as other pair
7. Replace by current source
** When we separately design EA, there are no more information about core voltage from core cell  replace core devices by current sources and just need to evaluate the optimized core current
4. Need to choose (fg, stk & m – multi) to adapt both min & max current consumption from load system

## Slide 9
Core
Constraint of variable names |  |  |  | 
Device | L (m) | Number of finger | Multiplier | Range of value
MPP | stk_core_mpp*60n | fg_core_mpp | m_core_mpp | 
MND1 | stk_core_nd1*60n | fg_core_nd1 | 1 | 
MND2 |  |  | 1 | 
MN1 | stk_core_n1*60n | fg_core_n1 | 1 | 
MN2 |  |  | 1 | 
MN3 | stk_core_n3*60n | fg_core_n3 | 1 | 
MN4 |  |  | 1 | 
MP3 | stk_core_p3*60n | fg_core_p3 | 1 | 
MP4 |  |  | 1 | 
ibn |  |  |  | 
ibp |  |  |  | 
rm |  |  |  | 
cm |  |  |  | 
Constraint of variable names |  |  |  | 
Device | L (m) | Number of finger | Multiplier | Range of value
MPP | stk_core_mpp*60n | fg_core_mpp | m_core_mpp | 
MND1 | stk_core_nd1*60n | fg_core_nd1 | 1 | 
MND2 |  |  | 1 | 
MN1 | stk_core_n1*60n | fg_core_n1 | 1 | 
MN2 |  |  | 1 | 
MN3 | stk_core_n3*60n | fg_core_n3 | 1 | 
MN4 |  |  | 1 | 
MP3 | stk_core_p3*60n | fg_core_p3 | 1 | 
MP4 |  |  | 1 | 
ibn |  |  |  | 
ibp |  |  |  | 
rm |  |  |  | 
cm |  |  |  | 
**Note:
UPDATE
** finger width = 200n

## Slide 10
Core
Schematic config |  |  |  | Modify in python
Device | L (m) | Number of finger | Multiplier | 
MPP | stk_core_mpp*60n | fg_core_mpp | m_core_mpp | -
MND1 | stk_core_nd1*60n | fg_core_nd1 | 1 | -
MND2 |  |  | 1 | -
MN1 | stk_core_n1*60n | fg_core_n1 | 1 | -
MN2 |  |  | 1 | -
MN3 | stk_core_n3*60n | fg_core_n3 | 1 | -
MN4 |  |  | 1 | -
MP3 | stk_core_p3*60n | fg_core_p3 | 1 | -
MP4 |  |  | 1 | -
ibn |  |  |  | -
ibp |  |  |  | -
rm |  |  |  | 
cm |  |  |  | 
Schematic config |  |  |  | Modify in python
Device | L (m) | Number of finger | Multiplier | 
MPP | stk_core_mpp*60n | fg_core_mpp | m_core_mpp | -
MND1 | stk_core_nd1*60n | fg_core_nd1 | 1 | -
MND2 |  |  | 1 | -
MN1 | stk_core_n1*60n | fg_core_n1 | 1 | -
MN2 |  |  | 1 | -
MN3 | stk_core_n3*60n | fg_core_n3 | 1 | -
MN4 |  |  | 1 | -
MP3 | stk_core_p3*60n | fg_core_p3 | 1 | -
MP4 |  |  | 1 | -
ibn |  |  |  | -
ibp |  |  |  | -
rm |  |  |  | 
cm |  |  |  | 
**Note:
UPDATE

## Slide 11
Core - example
stk_core_p3 fp_core_p3
stk_core_nd1 fp_core_nd1
Total length = stk * 60n (stk is integer number (1, 2, …)
Min finger width
n.o fingers, *0.5 means we want 60n per step
Keep multi=1, except MPP
Automatically adjust
stk_core_n1 fp_core_n1
stk_core_n3 fp_core_n3
Fixed value
stk_core_mpp fp_core_mpp m_core_mpp
rm
cm
ibp
ibn

## Slide 12
Core - testbench
Should use the same instance name of example
DC source
VDD source: DC=vddval AC=1 VREF source: DC=vrefval AC=0
Offset = 0.1*vddval min_load = 8000 ohm max_load = 16 ohm

## Slide 13
Core - testbench
Should use the same instance name of example
Lib: analigLib cell name: iprobe instance name: IPRB0

## Slide 14
Core - testbench
Used to check DCOP and AC of max_load verification
Used to check DCOP and PSR of min_load verification
Used to check LINE REGULATION and VOUT_ERR for both min & max load verification
Used to check LOAD REGULATION & VOUT_ERR

## Slide 15
Core - testbench
Testbench | Item | Parameter | Measurement | Unit
DCOP | Region | region_core_nd1 | OP("/core_maxload/MND1" "region") | 
 |  | vod_core_nd1 | abs(OP("/core_maxload/MND1" "vgt")) | 
 |  | vmarg_core_nd1 | OP("/core_maxload/MND1" "vsat_marg") | 
Transient | Line regulation | vout_vinmax_maxload | value(vtime('tran "/vreg_4") 9.98e-07) | 
 |  | vout_vinmin_maxload | value(vtime('tran "/vreg_4") 8e-09) | 
 |  | LNR_maxload | ((abs((vout_vinmax_maxload - vout_vinmin_maxload)) / 0.24) * 1000) | 
 |  | vout_vinmax_minload | value(vtime('tran "/vreg_5") 9.98e-07) | 
 |  | vout_vinmin_minload | value(vtime('tran "/vreg_5") 8e-09) | 
 |  | LNR_minload | ((abs((vout_vinmax_minload - vout_vinmin_minload)) / 0.24) * 1000) | 
 |  | LNR | max(LNR_maxload, LNR_minload) | 
 | Load regulation | vout_minload | value(vtime('tran "/vreg_5") 9.98e-07) | 
 |  | vout_maxload | value(vtime('tran "/vreg_5") 8e-09) | 
 |  | LDR | ((abs((vout_minload - vout_maxload)) / 0.0499) * 1000) | 
Testbench | Item | Parameter | Measurement | Unit
DCOP | Region | region_core_nd1 | OP("/core_maxload/MND1" "region") | 
 |  | vod_core_nd1 | abs(OP("/core_maxload/MND1" "vgt")) | 
 |  | vmarg_core_nd1 | OP("/core_maxload/MND1" "vsat_marg") | 
Transient | Line regulation | vout_vinmax_maxload | value(vtime('tran "/vreg_4") 9.98e-07) | 
 |  | vout_vinmin_maxload | value(vtime('tran "/vreg_4") 8e-09) | 
 |  | LNR_maxload | ((abs((vout_vinmax_maxload - vout_vinmin_maxload)) / 0.24) * 1000) | 
 |  | vout_vinmax_minload | value(vtime('tran "/vreg_5") 9.98e-07) | 
 |  | vout_vinmin_minload | value(vtime('tran "/vreg_5") 8e-09) | 
 |  | LNR_minload | ((abs((vout_vinmax_minload - vout_vinmin_minload)) / 0.24) * 1000) | 
 |  | LNR | max(LNR_maxload, LNR_minload) | 
 | Load regulation | vout_minload | value(vtime('tran "/vreg_5") 9.98e-07) | 
 |  | vout_maxload | value(vtime('tran "/vreg_5") 8e-09) | 
 |  | LDR | ((abs((vout_minload - vout_maxload)) / 0.0499) * 1000) | 

## Slide 16
Core - testbench
Testbench | Item | Parameter | Measurement | Unit
AC |  | UGB | cross(db(mag(getData("loopGain" ?result "stb"))) 0 1 "either" nil nil) | 
 |  | Av | value(db(mag(getData("loopGain" ?result "stb"))) 1) | 
 |  | PM | value(phaseDegUnwrapped(getData("loopGain" ?result "stb")) cross(db(mag(getData("loopGain" ?result "stb"))) 0 1 "either" nil nil)) | 
 |  | PSR_10k_maxload | abs(value(db(vfreq('ac "/vreg_1")) 10000)) | 
 |  | PSR_1meg_maxload | abs(value(db(vfreq('ac "/vreg_1")) 1000000)) | 
 |  | PSR_10k_minload | abs(value(db(vfreq('ac "/vreg_2")) 10000)) | 
 |  | PSR_1meg_minload | abs(value(db(vfreq('ac "/vreg_2")) 1000000)) | 
Testbench | Item | Parameter | Measurement | Unit
AC |  | UGB | cross(db(mag(getData("loopGain" ?result "stb"))) 0 1 "either" nil nil) | 
 |  | Av | value(db(mag(getData("loopGain" ?result "stb"))) 1) | 
 |  | PM | value(phaseDegUnwrapped(getData("loopGain" ?result "stb")) cross(db(mag(getData("loopGain" ?result "stb"))) 0 1 "either" nil nil)) | 
 |  | PSR_10k_maxload | abs(value(db(vfreq('ac "/vreg_1")) 10000)) | 
 |  | PSR_1meg_maxload | abs(value(db(vfreq('ac "/vreg_1")) 1000000)) | 
 |  | PSR_10k_minload | abs(value(db(vfreq('ac "/vreg_2")) 10000)) | 
 |  | PSR_1meg_minload | abs(value(db(vfreq('ac "/vreg_2")) 1000000)) | 
Example:

## Slide 17
Core - testbench
DCOP analysis
AC analysis
TRANSIENT analysis
STB analysis
 Execute these analyses in parallel

## Slide 18
Testbench | Parameter | Description | Specification | Unit
DC |  | Overdrive voltage (Vgs – Vth) | for all mosfet | 
 |  | Margin voltage (Vds-Vdsat) | for all mosfet | 
Transient |  | Output voltage error (max load) |  | 
 |  | Line regulation, variation of Vin (min & max load) |  | 
 |  | Load regulation, iload varies from max to min |  | 
AC |  | Unity Gain Bw |  | 
 |  | DC Loop Gain |  | 
 |  | Phase Margin of loop |  | 
 |  | Power Supply Rejected Ratio |  | 
Testbench | Parameter | Description | Specification | Unit
DC |  | Overdrive voltage (Vgs – Vth) |  | 
 |  | Margin voltage (Vds-Vdsat) |  | 
Transient |  | Output voltage error (max load) |  | 
 |  | Load regulation, iload varies from max to min |  | 
AC |  | Unity Gain Bw |  | 
 |  | DC Loop Gain |  | 
 |  | Phase Margin of loop |  | 
 |  | Power Supply Rejected Ratio |  | 
Core Specification

## Slide 19
Core Specification
After pass all the requirement (DCOP, Trans, AC)
Note:
total current consumption of LDO;
PSR@1MHz abs value of PSR at f=1MHz in db.
Example:
+
UPDATE